## Slide 1: Achieving equilibrium in the Soil Water Characteristic Curve: An ‘effective’ approach
S.E. Vero1,2, R. E. Creamer1, M.G. Healy2, T. Henry3, P. Forristal1, K.G. Richards1 & O. Fenton1
1Teagasc, Johnstown Castle, Environment Research Centre, Co. Wexford, Ireland.
2 Civil Engineering, National University of Ireland, Galway, Ireland.
3Earth & Ocean Sciences, National University of Ireland, Galway, Ireland.
.

## Slide 2: Soil Water Characteristic Curve
Relationship between pressure (Ψ) and water content (θ)

## Slide 3: Soil Water Characteristic Curve
Uses:
  Pore size distribution
  Plant available water
  Numerical modelling
Soil Hydraulic Parameters
θr θs α n m

## Slide 4: Measurement

## Slide 5: Centrifuge Method
Gardner Equation (Gardner, 1937)
ω = angular velocity (rad)
ϕ = matric suction (kPa)
ρ = density of pore fluid (g cm3)
g = acceleration due to gravity
r1 = radial distance to midpoint of specimen (cm)
r2 = radial distance to free water surface (cm)
Notes: First proposed by Briggs and McClane 1907, and further developed by Russell and Richards 1938
Limited availability of commercial benchtop centrifuges prior to Beckman Coulter’s purchase of SpinCo in 1954 and subsequent improvements in both the availability and capacity of such instruments, surely contributed to the establishment of slower methods such as pressure plates as de rigeour.

## Slide 6: Equilibrium
Intact soil cores vs. disturbed samples
Small samples
Disturbed
In-flight instruments
‘All of the water in the soil has the same value of free energy’
  No hydraulic gradient
  No flow
Notes: Dexter et al 2012 - Geoderma

## Slide 7: Rules of Thumb Disturbed Samples
2 Hours – Khanzode et al., 2002 (12 mm)
2 Hours – Russell and Richards (5 mm)
4-8 Hours – Smagin 2012 (10-15 g)

## Slide 8: Rules of Thumb Intact Samples
Until dewatering ceases? – Reis et al., 2011
3-8 Hours – Nimmo et al., 1987 (38 mm) – steady state flow
3-72 Hours – Nimmo 1990(38 mm) – in-flight instruments
>80 Minutes – da Silva and de Azevedo 2002 (50 mm)

## Slide 9: Objectives
Using the SWCC as input data (RETC and Hydrus 1D) to determine time lag in two vulnerable watersheds
How long should I centrifuge my samples?

## Slide 10: Initial Testing
Four intact soil cores
  Sand 40%
  Silt 36%
  Clay 24%
  Bulk density 1.35 – 1.47 g cm3
No predetermined experimental duration
Samples weighed every hour

## Slide 11: Dewatering

## Slide 12: Effective Equilibrium
Almost impossible in practice to identify true equilibrium
What does this mean for numerical modelling?
Is there an Effective Equilibrium?
Grassland and arable soil
3x4 soil cores
1 m2 area
0, -50, -100, -150, -200, -1000 and -1500 Kpa
24 hours, 48 hours and 72 hours

## Slide 13
Grassland | 
Sand (%) | 33
Silt (%) | 31
Clay (%) | 36
Bulk Density (g cm3) | 0.86
Arable | 
Sand (%) | 43
Silt (%) | 24
Clay (%) | 33
Bulk Density (g cm3) | 0.93

## Slide 14: Soil Water Characteristic Curves

## Slide 15: Soil Water Characteristic Curves

## Slide 16: VGM Parameters
Grassland |  | Arable | 
Treatment effect | Significance Level | Treatment effect | Significance Level
Pressure | *** | Pressure | ***
Treatment | *** | Treatment | ***
Pressure x Treatment | n.s | Pressure x Treatment | n.s
Treatment | Estimate | Treatment | Estimate
24-h | 64a† | 24-h | 67a
48-h | 61b | 48-h | 62b
72-h | 59c | 72-h | 61b
† Letters in common for each site indicate no significant difference between treatments (P<0.05) *** significant at P<0.0001, n.s non-significant |  |  | 

## Slide 17: Conclusions
24 hour treatment underestimates water content in undisturbed cores
Close similarities between 48 and 72 hour treatments
Effective Equilibrium

## Slide 18
Thank you
Any questions?